Levers

- A lever is a simple machine which helps us to do work with less effort.  A lever is any shaft which rotates around a fixed point.  Look at the following picture to understand the parts of a lever:

- Fulcrum = the point about which the lever rotates.

- Effort Arm = the distance from the fulcrum to the effort end.

- Resistance Arm = the distance from the fulcrum to the resistance end.

- When a machine makes it easier to move object we say that the machine has mechanical advantage.

- Mechanical advantage is the number of times a simple machine will multiply the input force.  The bigger the mechanical advantage, the more force goes into moving the resistance ( the thing being lifted)

This lever has a mechanical advantage of 1.

This lever has a mechanical advantage of 10.

- To calculate Mechanical advantage mathematically use this formula:

Length of effort arm

MA =	-----------------------------

Length of resistance arm

- There are three types of levers:

- Type I = The fulcrum is in the middle (like a seesaw)

- Type II = the Resistance is in the middle (Like  a wheelbarrow)

- Type III = the Effort is in the middle (Like your forearm)

## Friction:

- Friction is a force which resists motion.  All machines have some friction.  This friction takes away from the machine’s mechanical advantage  This means that a machine with lots of friction is an inefficient machine.

- Friction is caused by rough surfaces rubbing on each other.

Microscopic view of gold				Microscopic view of graphite

- A lubricant such as oil reduces friction.

# Text boxes

200 lbs. Of effort

200 pounds of resistance

200 pounds of resistance

20lbs. Of effort